## Slide 1
GHOST
Generator for Hardware-Oriented
Stealthy Trojans
An LLM-Powered Framework for Automated Hardware Trojan Design
arXiv 2412.02816

## Slide 2
Background: What Is a Hardware Trojan?
A Hardware Trojan (HT) is a malicious, hidden modification embedded directly into a chip's design — not software. Once fabricated, it lives inside the silicon and cannot be patched away.
What it is
Unauthorized logic inserted into RTL or netlist. Indistinguishable from normal circuit structure.
How it activates
A rare trigger condition — a secret input sequence — wakes it up. Completely dormant otherwise.
Why it's stealthy
Tiny area overhead, preserves normal behavior. Nearly impossible to detect via standard testing.
What it can do
Leak encryption keys, corrupt data, crash the system, degrade performance, or open a backdoor.
⚠ Growing threat: Globalized chip supply chains mean IPs pass through many potentially untrusted hands — the perfect window for a malicious integrator to insert a Trojan before fabrication.

## Slide 3
Threat Model: The Untrusted SoC Integrator
3PIP RTL
Designer
Delivers clean
IP core
SoC
Integrator
⚠ UNTRUSTED
Runs GHOST
CAD
Tools
Synthesis &
place-and-route
Foundry
Trusted
fabrication
Deployed
Chip
Trojan baked
into silicon
GHOST injects here
RTL Access
Integrators legally receive full RTL — no barriers to code inspection or modification
Time Pressure
Tight deadlines prevent deep manual review of complex third-party IP code
Trusted Foundry
The fab is assumed honest — all attacks occur at the RTL level before synthesis
GHOST bridges the knowledge gap — an attacker with RTL access but limited design expertise can leverage LLMs to quickly identify vulnerabilities and insert undetectable Trojans.

## Slide 4
Motivation: Why Existing HT Insertion Tools Fall Short
Prior automated HT tools all share fundamental limitations that GHOST is designed to overcome:
Tool
Agent Type
Limitation
Trust-Hub
Human
Manual insertion; slow, requires deep expertise, introduces human bias
TAINT / TRIT / FEINT / DTjRTL
Human-Config
Needs manual trigger/payload config; still design-specific, not truly general
MIMIC
ML
Requires large training datasets and significant compute; poor generalizability
ATTRITION / Trojan Playground
RL
Long training time per design; must retrain from scratch for new targets
TrojanForge
RL + GAN
High complexity and training cost; difficult to deploy outside its training domain
GHOST (this work)
LLM
Zero training needed; design-agnostic; fast; platform-agnostic ✓

## Slide 5
GHOST at a Glance: What It Does
GHOST feeds clean Verilog RTL into a large language model with a structured prompt. The LLM reads the design, finds a suitable insertion point, writes the Trojan code, and integrates it — all automatically. No training, no manual configuration.
Zero Training Required
LLMs arrive pre-trained on code. GHOST uses them zero-shot — just supply the RTL and a prompt. No datasets, no fine-tuning.
Platform & Design Agnostic
Works on ASIC and FPGA flows. Compatible with any synthesizable Verilog design regardless of size or domain.
RTL-Level Insertion
Operates directly on RTL source code — before synthesis — so Trojans survive to silicon and are invisible to gate-level tools.
Fully Automated End-to-End
Clean RTL in → Trojan-infected RTL out. The LLM handles analysis, attack-point selection, code generation, and integration.
GHOST turns an LLM into an autonomous hardware security attacker — no expertise required from the attacker

## Slide 6
Four Hardware Trojan Vulnerability Types
GHOST supports four functionally distinct Trojan classes. Each targets a different security objective:
T1
Change Functionality
Secretly alters the circuit's computation — wrong encryption output, privilege escalation, faulty arithmetic
Trigger: Activated by a specific rare input sequence invisible during normal operation
Example: AES core silently outputs wrong ciphertext after a secret 128-bit pattern is presented as input
T2
Leak Information
Creates a covert channel that transmits sensitive internal data (keys, states) to an attacker-observable output
Trigger: A benign-looking signal going high silently mirrors internal state to an extra output port
Example: AES encryption key k0 is streamed to trojan_out port whenever secret_trigger=1, invisible to normal testbenches
T3
Denial of Service
Permanently disables or crashes the module after a rare trigger condition is met
Trigger: A specific memory address accessed N consecutive times, or an internal counter reaching a threshold
Example: SRAM controller locks up and becomes unresponsive after address 8'hAA is accessed 15 times consecutively
T4
Performance Degradation
Deliberately slows down the circuit or increases power consumption without disabling it, evading functional tests
Trigger: A timing-sensitive condition or counter-based event that switches the design into a degraded operating mode
Example: UART baud-rate divider is silently doubled on trigger, halving throughput — the design still works but runs at half speed

## Slide 7
Contextual Trojan Prompts: One Per Vulnerability Type
Each Trojan type is driven by a tailored Contextual Trojan Prompt (CTP) that specifies the objective, mechanism, and stealth requirements:
T1
"Insert a subtle logic modification activated by a specific rare input sequence. The Trojan should alter critical data or control flow only when triggered."
T2
"Implement a covert channel that leaks sensitive internal data. Use a seemingly benign signal as the trigger, and encode the leaked data in a way that is hard to detect."
T3
"Implement a mechanism that disables the module after detecting a rare sequence of inputs, ensuring it is extremely rare to trigger during normal operation."
T4
"Insert a Trojan that degrades circuit performance on a rare trigger — introduce artificial delays, extra pipeline stages, or wasteful computation indistinguishable from legitimate design complexity."
Each CTP specifies: (i) clear objective · (ii) implementation style · (iii) trigger mechanism · (iv) stealth guidance

## Slide 8
Prompt Engineering: 3-Layer Strategy
GHOST stacks three distinct prompt layers in every API call to guide the LLM reliably through HT insertion:
Layer 1
Role-Based Prompting (RBP)
Sets the LLM persona as a hardware security expert. Primes domain-specific knowledge and maintains consistency across all HT types.
"You are a hardware security expert with extensive experience designing and implementing Hardware Trojans. Your task is to analyze the given hardware design and insert a stealthy HT that meets specific requirements."
Layer 2
Contextual Trojan Prompting (CTP)
Provides the specific HT objective (T1–T4), trigger style, payload description, and stealth requirements. Unique per vulnerability type.
"Implement a covert channel that leaks sensitive internal data. Use a seemingly benign signal as the trigger, and encode the leaked data in a way that is hard to detect."
Layer 3
Reflexive Validation Prompting (RVP)
Instructs the LLM to self-check its own output: verify correctness, confirm normal operation is preserved, and validate synthesizability before responding.
"Ensure all instructions are followed. Describe how the Trojan trigger and payload have been implemented. Verify the correctness, stealthiness, and synthesizability of the Trojan implementation."

## Slide 9
GHOST Framework Architecture
① Prompt Engineering
Role-Based Prompting (RBP)
→ Assigns LLM as HW security expert
Contextual Trojan Prompt (CTP)
→ T1 / T2 / T3 / T4 goals & trigger style
Reflexive Validation (RVP)
→ LLM self-checks its output
Clean RTL Design (Verilog)
→ Injected into the combined prompt
→
② LLM Inference
2.1 Model Selection
• GPT-4 (OpenAI) — closed-source
• Gemini 1.5 Pro (Google) — closed-source
• LLaMA3-70B (Meta / Groq) — open-source
2.2 LLM Tasks (sequential)
1
Analyze RTL design: understand structure & function
2
Identify best attack-point for insertion
3
Generate Trojan logic (trigger + payload)
4
Integrate HT into original RTL seamlessly
2.3 Response Extraction
→ HT-infected RTL · Trigger/Payload description · HT Taxonomy (type, location, mechanism)